## Slide 1: MICRO L’AFENTIKA
The Best

## Slide 2: Outline 01 02 03 04
Instruction Set Architecture
ALU Operations
Memory Instructions
Flow Control Instructions
05
Flow Control Instructions
Data Paths

## Slide 3: Instruction Set Architecture
Micro L’Afentika is a 16-bit microprocessor
16 registers
It has 28 addressable data memory locations
It operates on 16-bit instructions
It can perform 16 distinct instructions that spread across 3 categories
We will look at that in a bit (1,0)

## Slide 4: The Instructions and Their Opcodes
Add | Subtract | Multiply | Divide | AND | OR | XOR | Negate
0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111
Beq | Bne | Jump | ADDi | load | store | ORi | ANDi
1000 | 1001 | 1010 | 1011 | 1100 | 1101 | 1110 | 1111

## Slide 5: Control Unit
The CU is the brain of the brain, to put it.
It gives signals and controls what exactly happens when instructions are executed
The control unit takes bits 0, 1, 2 and 15 (opcodes) of all instructions and generate appropriate signals to control the following:
    - ALU Operations
    - Register Write Enable
    - Memory Write Enable
    - MUX Select Controls
    - Flow control signals

## Slide 6: Control Unit
Truth table for creating the circuit of the control unit:

## Slide 7: General ALU Operations (With only Register Locations)
All ALU instructions have 4 different parts
  - The opcode
  - 3 register locations specified with 4 bits each
The format
1 Bit | 4 bits | 4 bits | 4 bits | 3 bits
Opcode | Destination | Source 2 | Source 1 | Opcode
15 | 14:11 | 10:7 | 6:3 | 2:0

## Slide 8: ALU Instructions

## Slide 9: ALU Instructions with Immediate
These allow the user to also enter at most one operand as part of the instructions
This is possible for only three ALU operations:
      - AND
      - OR
      - ADD
      3. Instruction Format
Bits | 15 | 14:11 | 10:7 | 6:3 | 2:0
Description | Opcode | Destination | Immediate | Source Operand 1 | Opcode
Number of bits | 1 | 4 | 4 | 4 | 3
ANDi | 1111 | ORi | 1110 | ADDi | 1011

## Slide 10: ALU (Intermediate) Instructions

## Slide 11: Memory Instructions
There are two instructions that allow the microprocessor to communicate with memory
The memory instructions are
    - Load instruction: moving data from memory to register
    - Store instruction: moving data from register to memory
    3. Instruction format of memory instructions:
Bits | 15 | 14:11 | 10:3 | 2:0
Description | Opcode | Register (Destination) | Memory Address (Source) | Opcode
Number of bits | 1 | 4 | 8 | 3
Bits | 15 | 14:7 | 6:3 | 2:0
Description | Opcode | Memory Address (Destination) | Register (Source) | Opcode
Number of bits | 1 | 8 | 4 | 3

## Slide 12: Memory Instructions

## Slide 13: Flow Control Instructions
There are two major instructions used to control the flow of the instructions
- Branch Instructions
- Unconditional Jump instruction
2.

## Slide 14: Flow Control Instructions
Branch Operations
The branch operations take two operands and a 4 bit program counter offset.
Branch Equal (Beq): if the operands are equal
Branch Not Equal (Bne): if the operands are not equal
Bits | 15 | 14:11 | 10:7 | 6:3 | 2:0
Description | Opcode | Offset (value to add to (PC + 1)) | Source Operand 2 | Source Operand 1 | Opcode
Number of bits | 1 | 4 | 4 | 4 | 3

## Slide 15: Branch Instructions

## Slide 16: Flow Control Instructions
Jump Operation
The Jump operations allow the program counter to point to a specific address of the instruction memory.
This allows the program to skip over some number of instructions
Bits | 15 | 14:11 | 10:3 | 2:0
Description | Opcode | Unused | New address of the program counter | Opcode
Number of bits | 1 | 4 | 4 4 | 3

## Slide 17: Jump Instructions

## Slide 18: Sample Programme
load reg1 mem[1]
load reg2 mem[3]
load reg3 mem[1]
load reg4 mem[2]
add reg5, reg3, reg2 ; reg5 = reg2 + reg3
add reg6, reg4, reg1 ; reg6 = reg1 + reg4
beq -3, reg3, reg4 ; goes back to line 5 if reg3 == reg4
sub reg7, reg4, reg2 ; reg7 = reg2 – reg4
jmp 10 ; move to instruction number 11 (index starts at 0)
mul reg8, reg3, reg1 ; reg8 = reg1 x reg3 (never executed)
addi, reg9, 3, reg4 ; reg9 = reg4 + 3

## Slide 19: Thanks!